## INSTRUCTIONS FOR INSTALLING  FIXED DECK MOUNTED MOORING WHIPS   Customer Service: 954-298-4890

## Each support should be as close as possible in line with the bow and stern boat cleats. Mount pole support bases with 3/8” ss or galvanized lag bolts length will depend on the thickness of your deck. Drill a pilot hole for lag bolts or a clearance hole for through bolts. Washers should be used for lag bolts and on both sides of the through bolts (Mounting hardware not included). For concrete use appropriate mounting hardware. Insert the 1” pole into the base. Thread about half of the line through the pulley hold lines together at the base end of the pole insert the attached square on the end of the 1” pole into the bases. The looped end of the line attaches to your boat cleats. The straight end of the line goes through the hole in the support mounted cleat tie the end of the line so the line will stay attached to the cleat. Attach separate dock lines both for the bow and the stern adjust for desired distance for your boat from the dock (see sketch), tighten whip lines enough to keep your boat away from the dock secure the line on support cleat. Crossing spring lines may be added from the dock to your boat if you experience strong currents or high winds. The sketch below is a suggestion other mounting arrangements may be used depending on the position of your boat.

## Thank you for purchasing our products. After using our product and you are completely satisfied, we would like other potential customers to know about your wise choice. So, we would appreciate it if you go back to where you purchased your whips and leave a (hopefully favorable) review. We know your time is valuable so as an incentive we will provide to you our extended 2 yr. warrantee a value of $50.00 at no charge.