## INSTRUCTIONS FOR INSTALLING

## FIXED PILING MOUNTED MOORING WHIPS

## For piling mounting select a left and right support, the pole should be angled towards your boat. Each support should be as close as possible in line with the bow and stern boat cleats. Supports may be mounted on either left or right side of the piling.  It is not necessary to line up your boat cleats exactly. The whips and line will bend in any direction. The supports may also be rotated around the piling angling the whip either closer or further away from your intended boat cleats.

## Mount support approx. 2-3 feet above deck on piling or a few inches below the top of the piling(chest height). Mount with ½” ss or galvanized lag bolts 4” to 5” long depending on the condition of the piling. Mount directly to the piling face remove any decorative material like slates or obstructions. Mark top hole, drill under sized pilot hole (suggested 3/8 to7/16” depending on the condition if poor the smaller the drill) mount support with top hole not completely tight then drill bottom hole when support is in place and vertical. Then tighten both bolts firmly.

## Assemble whip poles: insert 1” pole into aluminum coupling tighten set screw. Thread line through pulley (about half way) hold lines together with pole, insert pole into base. The looped end attaches to your boat dock side cleats. Insert the cut off end of the line through the plastic cleat then tie a knot. Attach the looped end to the dockside of the boat cleats

## Attach separate dock lines both for the bow and the stern adjust for desired distance away from the dock approx.. 3’-4’  spring lines may be installed for strong currents or strong winds , tighten whip lines enough to keep your boat away from the dock secure line on support cleat adjust at low tide readjust at high tide. The sketch below is a suggestion other mounting arrangements may be used depending on the position of your boat. Customer service call 954-298-4890

## Thank you for purchasing our products. After using our product and you are completely satisfied, we would like other potential customers to know about your wise choice. So, we would appreciate it if you go back to where you purchased your whips and leave a (hopefully favorable) review. We know your time is valuable so as an incentive we will provide to you our extended 2 yr. warrantee a value of $50.00 at no charge.